## Slide 1: Quantifying Electrostatic Fields at Protein Interfaces Using Classical Electrostatics Calculations
Andrew W. Ritchie
Adviser: Lauren J. Webb
The University of Texas at Austin
Department of Chemistry
Notes: Hi, my name is Andrew Ritchie and today I will be discussing my dissertation research: Quantifying Electrostatic Fields at Protein Interfaces using Classical Electrostatics Calculations

## Slide 2: Why Study Protein Electrostatics?
≥ +25 MV/cm
≤ -25 MV/cm
GTPase
Effector
Notes: Doing a simple Poisson-Boltzmann electrostatics calculation on a protein shows that the electrostatic topology is very heterogeneous. This is demonstrated by the structure on the left, p21 Ras bound to Ral, where the protein complex has been opened like a book, so the figure on the top is looking at the binding surface of Ras from the perspective of Ral and the figure on the bottom is the binding surface of Ral from the perspective of Ras. Here we have mapped the component of the electrostatic that is perpendicular to the surface to the surface. We can see that the field is not only heterogeneous, but spans a large range, more than 50 MV/cm.
So if protein electrostatics are important, how do we experimentally look at them?

## Slide 3: Quantifying Electrostatic Fields at Protein Interfaces Using Classical Electrostatics Calculations
Ritchie, A. W. J. Phys Chem B 2013.
  Ritchie, A. W. J. Phys Chem B submitted
Ragain, C. M. J. Phys Chem B 2012.
Ritchie, A. W. J. Phys Chem B 2014.
Multi-Dimensional Umbrella Sampling
Numeric Poisson-Boltzmann Equation vs Reaction Field Method
Select Explicit Water in Poisson-Boltzmann
Atomic Multipole Optimized Energetics for Biomolecular Applications (AMOEBA)
Notes: My overall goals are to produce a method for calculating protein electrostatics which reproduces experimental measurements with enough confidence that we can use computation as an indicator of interesting experiments, and possibly replace expensive in vitro protein experiments with cheaper in silico experiments. To this aim, I have looked at multidimensional umbrella sampling as an enhanced MD method, different ways of solving the Poisson-Boltzmann equation, and explicit modeling of atomic polarizations via the AMOEBA force field. Today I’m mostly going to focus on my PB results.
----- Meeting Notes (8/5/15 16:06) -----
Went through this too fast. It's really the summary of everything I have done. Add citations to papers. This is not translating to that fact that this is projects that I have worked on. Try to make this more big-picture.

## Slide 4: Outline
Vibrational Stark Effect
System: Rap1a Docked to RalGDS
Protein Electrostatic Fields
Poisson-Boltzmann vs Reaction Field Method
Select Explicit Water
Electronic Polarizability: AMOEBA
Importance of Protein Electrostatics
Notes: We look at protein electrostatic fields using the vibrational stark effect

## Slide 5: Probing Protein Electrostatics Using the Vibrational Stark Effect (VSE)
Notes: The VSE is a way to relate changes in electrostatic fields perpendicular to some vibrational chromophore dipole moment with changes in vibrational absorption energy. In our case, we are looking at cyanocysteine as our vibrational chromophore.
Don’t spend too long on this: VSE is a way to relate changes in electrostatic fields with vibrational absorption energy shifts
----- Meeting Notes (8/5/15 16:06) -----
Try not to say red and blue shift, try to say increase and decrease absorption energy.

## Slide 6: Outline
Importance of Protein Electrostatics
Vibrational Stark Effect
System: Rap1a Docked to RalGDS
Protein Electrostatic Fields
Poisson-Boltzmann vs Reaction Field Method
Select Explicit Water
Electronic Polarizability: AMOEBA
Notes: So we know how to measure protein fields. Now let me take a moment to introduce our experimental system.

## Slide 7: Why Study Protein Electrostatics?
Ragain, et al., J. Phys. Chem. B 2012
Huang, et al., Nat. Struct. Bio. 1998
Nassar, et al., Nat. Struct. Bio. 1996
Notes: To do so, I first need to mention structure. Here we see two GTPases, p21 Ras (red) and Rap1a (blue), where the backbones have been aligned. Structurally, they are nearly identical. However, they bind the downstream effector, Ral Guanosine Dissociation Stimulator, with an order of magnitude difference in dissociation constant. Because they are so structurally similar, electrostatics must be responsible for this selectivity.
50% amino acid identity
80% amino acid homology
0.7 Å effector binding surface RMSD
----- Meeting Notes (8/5/15 16:06) -----
Say "Protein electrostatics are the forces caused by the orientation and locations of charges in space, as related to proteins". I'm not telling them what electrostatics are.

## Slide 8: System: GTPases Rap1a and p21 Ras, Each Docked to RalGDS
1GUA:
Rap1a
Raf
1LFD:
p21 Ras
RalGDS
Notes: On the left is the crystal structure of Rap1a docked to Raf, 1GUA, and p21 Ras docked to RalGDS, 1LFD.
----- Meeting Notes (8/5/15 16:06) -----
On the top is the GTPase and on the bottom is the effector. What we're looking at is the docking of the GTPase to the effector.
WT Rap/Ral:

## Slide 9: System: GTPases Rap1a and p21 Ras, Each Docked to RalGDS
1GUA:
Rap1a
1LFD:
RalGDS
Notes: In the work I’m going to present, I am looking exclusively at Rap1a docked to its downstream effector, RalGDS.

## Slide 10: Goal: Validate Computational Electrostatic Techniques Against Experimental Stark Shifts
N27
G28
N29
Y31
K32
N54
Rap1a
Ralβ
Ragain, et al., J. Phys. Chem. B 2012
Lysine (WT)
Glutamic Acid
K31E
E30D
Glutamic Acid
Aspartic Acid
Notes: As I mentioned before, we are using VSE to look at electrostatic fields at the protein-protein interface. To do so, we have made six different Ral systems, each with a mutation from one interface amino acid to cyanocysteine.
…
Rap K31E (and E30D/K31E) have a Kd of 1.8 and 1.0, respectively
----- Meeting Notes (8/5/15 16:06) -----
"We were interested in for physiological reasons in mutations on 30 and 31..."

## Slide 11: Goal: Validate Computational Electrostatic Techniques Against Experimental Stark Shifts
Ragain, et al., J. Phys. Chem. B 2012
Ragain, et al., J. Phys. Chem. B 2012
Notes: ----- Meeting Notes (8/5/15 16:06) -----
ALWAYS TELL US WHAT WE ARE LOOKING AT, don't let the audience get tricked into trying to interpret the bar chart.

## Slide 12: Computational Approach
PDB Structure
T initial
T final
MD Ensemble
Electrostatic Field
≥ +1.5
MV/cm-1
≤ -1.5
MV/cm-1
Electrostatics Model
Compare to Experiment
Assess, Iterate, & Formulate New Hypothesis
Notes: 1. something people can use to predict interesting experiments
2. better molecular understanding and therefore ability to ask interesting physics questions

## Slide 13: Computational Approach
Assess, Iterate, & Formulate New Hypothesis
Compare to Experiment
PDB Structure
T initial
T final
MD Ensemble
Electrostatic Field
≥ +1.5
MV/cm-1
≤ -1.5
MV/cm-1
Electrostatics Model
Notes: 1. something people can use to predict interesting experiments
2. better molecular understanding and therefore ability to ask interesting physics questions

## Slide 14: Enhanced Molecular Dynamics: Umbrella Sampling
χ1 (Degrees)
χ2 (Degrees)
Notes: Mention the log scale bar

## Slide 15: 2D-probability distributions: a test case
High Probability
Low Probability
Notes: Now one of the first things I wanted to do after deciding to do a 2D sampling strategy was to make sure I knew what to expect from an alkane-like molecule and test the Weighted Histrogram Analysis code my group uses on a 2D system.
To do this I modeled a fictional molecule in which the only contribution to its energy are the chi1 and chi2 dihedral angles, which were each modeled independently using a Ryckaert-Belleman potential function. The main point I wanted to show here is that in 2 dimensions, the probability looks like the product of the 1 dimensional probabilities for an alkane molecule and that, for a perfect test case, I can reproduce the analytic probability distribution.

## Slide 16: Simulation Convergence: Tracking The Field
Numeric
RFM
Total Simulation Time (ns)

## Slide 17: Simulation Convergence: Tracking The Field
Numeric
RFM
Total Simulation Time (ns)

## Slide 18: Outline
Importance of Protein Electrostatics
Vibrational Stark Effect
System: Rap1a Docked to RalGDS
Protein Electrostatic Fields
Poisson-Boltzmann vs Reaction Field Method
Select Explicit Water
Electronic Polarizability: AMOEBA
Notes: Now that we have ensembles of structures, let’s move on to electrostatics calculations

## Slide 19: Computational Approach
Assess, Iterate, & Formulate New Hypothesis
Compare to Experiment
PDB Structure
T initial
T final
MD Ensemble
Electrostatic Field
≥ +1.5
MV/cm-1
≤ -1.5
MV/cm-1
Electrostatics Model
Notes: Let me remind you that we’ve used a refinement approach for how we go about calculating electrostatic fields. This means that we may have started with a single method (PB), but we used the results of that to formulate new hypotheses on the sort of changes that may be required to improve the veracity of these sorts of calculations.

## Slide 20: Electrostatics Models
Poisson-Boltzmann Implicit Solvent |  | PB w/ Selected Explicit Water | 
 | Atomic Multipole Optimized Energetics for Biomolecular Applications (AMOEBA) |  | 

## Slide 21: Electrostatics Models
PB Implicit Solvent | PB w/ Selected Explicit Water | Explicit Solvent
AMOEBA | AMOEBA-CP | AMOEBA-CPf
Notes: ----- Meeting Notes (8/3/15 16:39) -----
Waaaaaaaaaay too much detail

## Slide 22: Linear Poisson-Boltzmann Equation

## Slide 23: Poisson-Boltzmann: Reaction Field Method (RFM)
Notes: We tried using PB straight-out-of-the-box and the results (absolute fields) were poor and inconsistent.
Removing the reference potential from the solvated potential results in only the potential generated by the solvent polarizing about the solute, represented by the rightmost image. The SRF (leftmost image) result being added to the analytical solution to the Coulomb field for all protein atoms in a dielectric solute, (middle image), resulting in a total field which uses a numeric solution for the contribution of the implicit solvent and an analytic solution for the contribution of the explicit solute. In this way, numerical errors in the final result are reduced by only solving for part of the system (the solvent) numerically. This also decreases the calculation sensitivity to input parameters such as box size, grid spacing, box location, charge mapping method, etc. Since our initial work, APBS now has the “lrpbe” keyword, which solves for the SRF directly without requiring a reference calculation.
APBS has a keyword that solves the PBE (using finite difference) in this manner (lrpbe)

## Slide 24
Original box
New box
PB Grid Location
Notes: Finally, I’m also working on a set a even coarser grid-spacings in which the second stage boxes encompass approximately half and approximately all of the protein each. The idea here is to determine whether the box size or the grid spacing is more important. I do not yet have any examined data for this strategy.
Because APBS is very highly tunable, one of the challenges is determining which parameters are most important and whether or not it’s physically reasonable. Right now, focusing on the box positions, I’m trying to come up with a consistent metric for determining how to decide the location, size, and grid spacing that is the most useful combination of accurate and quick.

## Slide 25: PB Grid Location: 60 Å, 0.25 Å Between Grid Points
Experimental Absorption Energy (cm-1)
Experimental Change in Absorption Energy (cm-1)
Calculated Field
(kbT/eÅ)
Calculated Change
in Field (kbT/eÅ)
Numeric Field
RFM Field

## Slide 26: PB Grid Location: Small Boxes
Red: Center of nitrile Cδ
Green: Shifted towards Ralβ center of mass
Blue: Shifted towards system center of mass

## Slide 27: PB Grid Location: 19 Å, 0.099 Å Between Grid Points
Experimental Absorption Energy (cm-1)
Experimental Change in Absorption Energy (cm-1)
Calculated Field
(kbT/eÅ)
Calculated Change
in Field (kbT/eÅ)
Numeric Field
RFM Field
Red: Center of nitrile Cδ
Green: Shifted towards Ralβ center of mass
Blue: Shifted towards system center of mass
Notes: Large box numeric weakly sensitive to grid location.
Large box RFM has higher correlation, shows sensitivity to box.
Correlations increased in numeric difference but not RFM difference

## Slide 28: PB Grid Location: 10 Å, 0.052 Å Between Grid Points
Experimental Absorption Energy (cm-1)
Experimental Change in Absorption Energy (cm-1)
Calculated Field
(kbT/eÅ)
Calculated Change
in Field (kbT/eÅ)
Numeric Field
RFM Field
Red: Center of nitrile Cδ
Green: Shifted towards Ralβ center of mass
Blue: Shifted towards system center of mass
Notes: Small box numeric VERY sensitive to box location
Small box RFM much less sensitive
Correlations increased in numeric difference but not RFM difference

## Slide 29: Conclusions
Center the grid on the region of interest; do not try to optimize the grid location. Instead opt for the highest feasible grid point density.
Use the numeric solution to the PB equation when trying to evaluate the difference in fields.
Use the RFM when the actual field values are important.

## Slide 30: PB: Including Selected TIP3P Water Molecules: 5 Å Water Sphere, Nearest, Hydrogen-Bonding
Le Questel, et al., J. Phys. Org. Chem. 2000
Schiffer, et al., J. Am. Chem. Soc. 2013
rNH ≤ 2.25 Å
NHO ≥ 138˚
Notes: Trying to be very generous with hydrogen bonding criteria

## Slide 31: PB Including Selected TIP3P Water Molecules: 5 Å Water Sphere
Experimental Absorption Energy (cm-1)
Experimental Change in Absorption Energy (cm-1)
Calculated Field
(kbT/eÅ)
Calculated Change
in Field (kbT/eÅ)
Numeric Field
RFM Field
Implicit Solvent
5 Å Water Sphere
Notes: Sphere does not help either calculation methods
Correlations increased in numeric difference but not RFM difference
If a water was within 5 Å of the nitrile, it remained within 5 Å for an average of 20±4.2 frames

## Slide 32: RalGDS Monomer: The only example of the 5 Å Water Sphere Improving Correlation
Experimental Absorption Energy (cm-1)
Calculated Field
(kbT/eÅ)
Numeric Field
RFM Field

## Slide 33: PB Including Selected TIP3P Water Molecules: Hydrogen-Bonding Water
Experimental Absorption Energy (cm-1)
Experimental Change in Absorption Energy (cm-1)
Calculated Field
(kbT/eÅ)
Calculated Change
in Field (kbT/eÅ)
Numeric Field
RFM Field
Implicit Solvent
Hydrogen-Bonding Water
Only 9.92% of frames had a nitrile-water hydrogen bond
Notes: H-bonding also does not help
Correlations increased in numeric difference but not RFM difference
9.92% of frames had a nitrile-water hydrogen bond

## Slide 34: PB Including Selected TIP3P Water Molecules: Nearest Water Molecule
Experimental Absorption Energy (cm-1)
Experimental Change in Absorption Energy (cm-1)
Calculated Field
(kbT/eÅ)
Calculated Change
in Field (kbT/eÅ)
Numeric Field
RFM Field
Implicit Solvent
Nearest Water
Notes: Nearest water does not help
Correlations increased in numeric difference but not RFM difference

## Slide 35: PB: Including Selected TIP3P Water Molecules
Percentage of Frames with a Nitrile-Water Hydrogen Bond
Average Number of Frames Water Remained within 5 Å of Nitrile

## Slide 36: Conclusion
Generally, do not include an explicit water sphere for a PB calculation. Although it can be beneficial, it must be justified after-the-fact and is subject to the quality of the water sampling.
In a system with little hydrogen-bonding to water, do not include those water molecules. Further study is required for generalizations about a system with more-significant hydrogen bonding.
Do not include the nearest water molecule.

## Slide 37: Explicitly Modeling Electronic Polarizability: AMOEBA

## Slide 38: AMOEBA Fields From Amber03 Structural Ensembles Are Less Correlated to Experiment than PB Fields
Notes: For systems where dynamics were generated in a point charge force field (Amber03), fields calculated via the polarizable AMOEBA force field are generally worse than those calculated using PB with point charges

## Slide 39: Conclusion
When calculating fields using the AMOEBA force field, dynamics should also be performed using AMOEBA. It is likely that the ensembles are not transferable; Amber03 includes orientational polarization (via MD), while AMOEBA incorporates both orientational (via MD) as well as electronic polarization; low energy orientations likely differ.

## Slide 40: Conclusions: Electrostatics Models
Do not explicitly include a solvent sphere or nearest water.
When hydrogen-bonding is rare, do not include hydrogen bonding water molecules.
Ensembles are not transferable
Sampling using the force field defining the electrostatic model
Center the grid on the region of interest and use the highest grid point density feasible
Use the numeric solutions to the PB equation for comparing differences in fields and the RFM for comparing actual field values
Poisson-Boltzmann Implicit Solvent |  | PB w/ Selected Explicit Water | 
 | Atomic Multipole Optimized Energetics for Biomolecular Applications (AMOEBA) |  | 

## Slide 41
Acknowledgements
Advisor
Lauren J. Webb, Ph.D.
Graduate Students
Cari Anderson
Jason Dugger
Whitney Fies
Jeremy First
Seth Norman
Elisa Novelli
Rebika Shrestha
Josh Slocum
Previous Graduate Students and Post Docs
Daniel Ensign, Ph.D.
Christina Ragain, Ph.D.
Amy Stafford
David Walker, Ph.D.
Undergraduates
Kelsey Eklund
Santiago Sanchez
Funding
Burroughs Welcome Fund
The Welch Foundation
The University of Texas at Austin
Collaborators
Pengyu Ren, Ph.D. (BME)
Michael Schnieders, Ph.D. (Iowa)
Facilities
TI3D
TACC

## Slide 42: Enhanced Molecular Dynamics: Umbrella Sampling

## Slide 43
Enhanced Molecular Dynamics: Umbrella Sampling

## Slide 44: Enhanced Molecular Dynamics: Umbrella Sampling

## Slide 45: The Case for Electronic Polarizability: AMOEBA
Notes: ----- Meeting Notes (8/3/15 16:18) -----
backup

## Slide 46: The Case for Electronic Polarizability: AMOEBA
Fried, S. D., et al. J Am Chem Soc 2013.
Ragain, Slocum, Eklund
Notes: ----- Meeting Notes (8/3/15 16:18) -----
Backup

## Slide 47: Calculating Fields in AMOEBA

## Slide 48: Potential, Field, and Induced Dipole Expressions

## Slide 49
Electrostatic Frame Clustering: Taking advantage of a weighted average

## Slide 50: Electrostatic Frame Clustering: Taking advantage of a weighted average

## Slide 51: MD: sampling methods
Cα
Cβ
Sγ
Cδ
N
  χ2
  χ1
Old (1D)
  χ1
  18 ns
New (2D)
  χ1 + χ2
  57.6 ns
Notes: The most impactful difference between sampling two degrees of freedom rather than one are the dipole moment vectors of the nitrile probe. The reason for using umbrella sampling is because there are potential energy barriers that are not likely to be surpassed over a reasonable simulation time at biologically relevant temperatures. The nitrile probe used has two relevant torsional degrees of freedom beyond the backbone. By just biasing a single degree of freedom, chi 2, an ensemble of structures are generated which nearly all have the same chi 1 dihedral and incompletely samples the 3 dimensional dipole vector space.
Using 2D umbrella sampling, however, creates a more-complete picture of probe dipole vectors, which is relevant for the magnitude of the VSE.

## Slide 52
2D-WHAM
Convert 2D-problem to 1D-problem
  Bin(0,0)=0, Bin(0,1)=1, …
  For 72x72 5o bins, 5184 total bins
Convert 1D python script to C++
Bug found! Fix and test against known potential
  Ryckaert-Bell alkane potential:
  Cn={9.28, 12.16, -13.12, -3.06, 26.24, -31.5}

## Slide 53
Stark turning rate and dielectric constant
Stark effect
Linear PBE